Position Update Distribution
(PUD)
OLSR Plugin

Changelog
Version	Date	Remarks
0.23	20111212	- Rework chapter 1
0.22	20111021	- Update for new Position Update Sentence Format and associated new OLSR Position Update Messages.
0.21	20110927	- Add AIS MMSI to 'Locally Unique / Experimental Identifiers'. / - Add URN to 'Locally Unique / Experimental Identifiers'.
0.20	20110616	- Add internal interfaces.
0.19	20110614	- Prepare document for publishing into olsrd git tree.
0.18	20110331	- Add section 'Input GPS Multicast Messages'. / - Add remarks about the number of bits and bytes in section 'Id Types'.
0.17	20110323	- Add IdType 194 to 'Locally Unique / Experimental Identifiers'. / - Add a note about sentence termination.
0.16	20110301	- Update description of validity time in Table 2. / - Renamed 'Validity Time' to 'Update Time'.
0.15	20110221	- Latitude and longitude are optional in the position update sentence. / - IdType range adjusted to [0, 254] in the position update sentence.
0.14	20101209	- Rename NBSGPS to PUD.
0.13	20101201	- Update HDOP range.
0.12	20101116	- Add paragraph 'Reserved for Future Use Identifiers'.
0.11	20101112	- Add changelog. / - Change 'course' to 'track' and update the example to show an integer. / - Clarify sea level to be mean sea level (geoid). / - Minor textual fixes.
0.10	20101111	- Initial Version.

# Overview
## Introduction
The Position Update Distribution (PUD) OLSR plugin has a number of functions:
- It distributes the (GPS) position of the router over the OLSR network.
- It transmits the position information of the router to a central (relay) server (this is an optional function).
These functions are discussed in the following paragraphs.
## Position Distribution over OLSR
Position distribution over the OLSR network is the main function of the PUD plugin. The process involved is depicted in the figure below and described after that.
The process:
Figure 1: PUD OLSR Plugin Overview
1. On Router 1, the GPS Daemon receives position information from its GPS antenna and sends multicast messages with that position information onto LAN 1 in the form of standard NMEA GPS sentences.
2. The PUD OLSR plugin receives these multicast messages by listening for them on LAN 1.
3. All NMEA GPS sentences in the received multicast messages are parsed for relevant information and converted to an internal binary format (on a per-message basis). The internal binary format is then used to transmit a position update over the OLSR network as an OLSR position update message.
4. On Router 2, upon reception of an OLSR position update message, the message is converted to a (proprietary/custom) NMEA sentence. Such a sentence will be referred to as a “position update sentence” (see page 7).
5. A position update packet, containing one or more position update sentences, is then sent as a multicast message onto LAN 2.
## Position Uplink
The secondary function of the PUD plugin is to send its position updates to a relay server (uplink the position). The process involved is depicted in the figure below and described after that.
The process is basically the same as that of distribution over the OLSR network, but instead of sending the position update to the OLSR network and receiving from the OLSR network, a Relay Server is used (steps 3 and 4).
Figure 2: PUD OLSR Plugin Overview
1. On Router 1, the GPS Daemon receives position information from its GPS antenna and sends multicast messages with that position information onto LAN 1 in the form of standard NMEA GPS sentences.
2. The PUD OLSR plugin receives these multicast messages by listening for them on LAN 1.
3. All NMEA GPS sentences in the received multicast messages (from LAN 1) are parsed for relevant information and converted to an internal binary format (on a per-message basis). The internal binary format is then used to transmit a position update as an OLSR position update message over the uplink to the Relay Server.
4. On Router 2, upon reception of an OLSR position update message from the downlink, the internal binary format is converted to a (proprietary/custom) NMEA sentence. Such a sentence will be referred to as a “position update sentence” (see page 7).
5. A position update packet, containing one or more position update sentences, is then sent as a multicast message onto LAN 2 and the position update is also sent onto the OLSR network.
## Relay Server
The exact working of the Relay Server are out-of-scope for this document and not even relevant.
It is sufficient to think of the Relay Server as a server that receives position updates and distributes the position updates to all the OLSR networks it knows about.
This architecture enables position distribution to out-of-range OLSR networks
## Cluster Leader Uplink and Position Update Downlink
In order have a more efficient distribution of position updates over several out-of-range OLSR networks the smart gateway mechanism of OLSR is employed:
- Each router continuously elects a smart gateway.
- The router sends, on a regular basis, its main IP address together with the main IP address of the chosen smart gateway onto the uplink in the form of a ClusterLeader message.
- The Relay Server now has enough information to determine which routers are in which OLSR network and which node in that network is chosen as a cluster leader.
- When the Relay Server receives a position update, it distributes this update to every cluster leader it knows about, except to the cluster leader of the network of which the router that sent the update is a member.
- When a router receives one or more position updates (from the Relay Server) on its downlink, then it sends these updates onto its LAN and onto its OLSR network.
This architecture lets each router uplink its position individually, while downlinking position updates is done only once per OLSR network (and letting the OLSR network further distribute the position updates to all routers in the OLSR network).
# External Interfaces
## Input GPS Multicast Messages
The GPS multicast messages that are sent by the GPS daemon in step 1 and received by the PUD OLSR plugin in step 2 of the process described above are expected to be in the format described below:
- A GPS multicast message has to start with the string '$GP',
- A GPS multicast message is expected to contain one or more (preferably more) NMEA GPS sentences,
- A NMEA GPS sentence starts with the string '$GP' and ends with the string '\r\n'.
- As many sentences as possible should be combined in a multicast message in order to provide as much GPS information to the plugin as possible: the plugin processes the multicast messages separately and does not aggregate them.
An example of a good GPS multicast message is shown below.
$GPRMC,141536.00,A,3208.86142,N,00320.78558,E,0.010,,020311,,,A*72\r\n
$GPVTG,,T,,M,0.010,N,0.018,K,A*2B\r\n
$GPGGA,141536.00,3208.86142,N,00320.78558,E,1,12,1.10,19.2,M,46.0,M,,*65\r\n
$GPGSA,A,3,29,08,02,05,30,04,07,13,16,10,23,20,1.99,1.10,1.66*01\r\n
$GPGSV,4,1,13,01,08,031,,02,46,273,51,04,44,215,33,05,21,296,48*73\r\n
$GPGSV,4,2,13,07,48,124,36,08,22,184,25,10,69,287,47,13,68,062,42*7C\r\n
$GPGSV,4,3,13,16,16,089,47,20,07,121,27,23,32,069,43,29,08,335,43*79\r\n
$GPGSV,4,4,13,30,11,021,36*4F\r\n
$GPGLL,3208.86142,N,00320.78558,E,141536.00,A,A*6B\r\n
## Position Update Packet Format
A position update packet can contain one or more position update sentences. When more than one sentence is present in the message then the sentences are simply concatenated. A simplified syntax description is:
packet = [sentence]+
Note:	Currently there is always a single sentence present in the message, but that can change without prior notice.
## Position Update Sentence Format
Position update sentences are used as part of a position update packet (see page 7). The detailed format (including an example) is shown below.
1	2	3	4	5	6	7	8	9	10	11	12	13	14	15
$PNBSX,	0,	0,	1.2.3.4,	1,	Node1,	300610,	090450,	256,	3208.86142,N,	320.78558,E,	12,	50,	19,	2.3
NMEA Prefix	Sentence Version	Gateway Flag	OLSR Originator	IdType	Id	Date	Time	Update Time	Latitude	Longitude	Altitude	Speed	Track	HDOP

Figure 1: Position Sentence Format Overview and Example
Note:	The commas that are shown in the example on the second row of Figure 1 are not part of the field values but of the NMEA format.
Note:	Fields that are colored yellow in Figure 1 are optional and can be empty, which indicates that the corresponding value is unknown or not present. An empty field will still have a comma as per the NMEA format.
Note:	Whitespace can be ignored in a position update sentence, except for the Id field.
Note:	Each sentence is always terminated with the '\r\n' character sequence.
### Sentence Version 1
Field Number	Field Name	Description
1	NMEA Prefix	The NMEA prefix of the sentence (configurable). / A string that starts with '$P' (default is '$PNBSX').
2	Sentence Version	The version of the sentence format. / An unsigned integer number (fixed value)
3	Gateway Flag	A flag indicating whether the position update originated from the plugin (0) or from an external gateway (1). / An unsigned integer number in the range [0, 1].
4	OLSR Originator	The OLSR originator IP address (can be an Ipv4 or Ipv6 address). / A string representation of an IP address.
5	IdType	The type of the Id field (configurable), describing the semantics of the Id field (see paragraph 2.4 on page 10). / An unsigned integer number in the range [0, 254].
6	Id	The Id of the sending node (configurable). / A string representation of the configured information (see paragraph 2.4 on page 10).
7	Date	The date of the information. / An unsigned integer number in the format 'DDMMYY'. / DD: Day [01, 31] MM: Month [01, 12] YY: Year [00, 99]
8	Time	The time of the information. / An unsigned integer number in the format 'HHMMSS'. / HH: Hours [00, 23] MM: Minutes [00, 59] SS: Seconds [00, 60][1]
9	Update Time	The number of seconds (counting from the date and time fields) after which the information will be sent again. / Without packet loss in the network the information can be considered invalid after this interval. To compensate for packet loss the receiver of the information can multiply the update time by a compensation factor (for example 3, which is a good value for most networks) to obtain the interval after which the information can truly be considered invalid. / An unsigned integer number in the range [0, 1015792], with zero meaning 'infinite'.
10	Latitude	Latitude and latitude‑hemisphere of the information. / A combination of an unsigned floating point number and a string in the format 'DDMM.SSSSS,H'. / DD: Degrees [0, 90] MM: Minutes [00, 59] SSSSS: Minutes Fraction[2] [0, 99999] H: Hemisphere N or S
11	Longitude	Longitude and longitude‑hemisphere of the information. / A combination of an unsigned floating point number and a string in the format 'DDDMM.SSSSS,H'. / DDD: Degrees [0, 180] MM: Minutes [0, 59] SSSSS: Minutes Fraction [0, 99999] H: Hemisphere E or W
12	Altitude	Altitude in meters above mean sea level (geoid). / A signed integer number in the range [-400, 65135].
13	Speed	Speed in kilometers per hour (km/h). / An unsigned integer number in the range [0, 4095].
14	Track	Direction of the movement of the information, in degrees relative to true north. / An unsigned integer number in the range [0, 359].
15	HDOP	Horizontal Dilution Of Precision. / An unsigned floating point number in the range [0.0, 40.94].
16	Checksum	The checksum of the complete string, not including the checksum itself. / The checksum is calculated exactly the same way as a checksum in a standard NMEA GPS sentence and is a hexadecimal number in the range [00, FF], preceded by a '*'. / This field is not shown in Figure 1.
17	Sentence Termination	The standard NMEA sentence terminator ('<cr><lf>' / '\r\n'). / This field is not shown in Figure 1.
[1] A value of 60 seconds indicates a leap second.
[2] Also explained as the fraction of (seconds / 60).

Table 2: Position Update Sentence Format Description
Note:	The ranges that are mentioned are indicative and represent the current ranges. These ranges depend upon the internal format that is used for position update messages on the OLSR network.
## Id Types
An Id Type describes the semantics of the Id field in a Position Update Sentence.
Its range of [0, 255] is split into 2 ranges: one range for globally unique identifiers and one range for local / experimental identifiers.
Beside the split ranges, the number 255 is reserved for future use.
### Globally Unique Identifiers
IdType Value	Type of Id / Description
0	The 48‑bit (6 bytes) universal LAN MAC address of the utilised OLSR interface on the sending node, as per the IEEE 802-2001 specification. / Represented as 'xx:xx:xx:xx:xx:xx', with x being a hexadecimal number.
1	An MSISDN number, as per the ITU-T E.164 specification (50 bits, 7 bytes). / Represented as an unsigned integer number with 15 digits.
2	A Tetra number, as per the ETSI TR 102 300-5 specification (57 bits, 8 bytes). / Represented as an unsigned integer number with 17 digits.
3	The DNS name of the sending node, as per the IETF RFC 1034 specification (variable length). / Represented as a text string.
4	IPv4 address of the utilised OLSR interface on the sending node. This can only occur when the OLSR stack runs in IPv4 mode, as per the IETF RFC 791 specification (32 bits, 4 bytes). / Represented in the regular dot notation for an IPv4 address.
5	Reserved
6	IPv6 address of the utilised OLSR interface on the sending node. This can only occur when the OLSR stack runs in IPv6 mode, as per the IETF RFC 2460 specification (128 bits, 16 bytes). / Represented in the regular dot notation for an IPv6 address.
7	An AIS MMSI number, as per the ITU M. 1371 specification (30 bits, 4 bytes). / Represented as an unsigned integer number with 9 digits.
8	A URN number, as per the Unit Reference Number specification at http://www.dtic.mil/cjcs_directives/cdata/unlimit/3156_01.pdf (24 bits, 3 bytes). / Represented as an unsigned integer number with 8 digits.
... 191	Reserved

Table 3: Globally Unique Identifiers
Note:	IdType values that are colored red in Table 3 are transmitted as‑is over the OLSR network: be advised that performance will be impacted when these values take more than about a dozen bytes.
### Locally Unique / Experimental Identifiers
IdType Value	Type of Id / Description
192	An unsigned integer number of 7 digits conforming to the SSI format described in 'Nationaal Nummerplan Brandweer Nederland, version 1.5, May 2008' (24 bits, 3 bytes).
193	An unsigned integer number of 6 digits conforming to the format described in 'Nationaal Nummerplan Ambulancezorg Nederland, version 5.0, April 2009' (20 bits, 3 bytes).
194	An unsigned integer number of 4 digits in the range [1, 8191] (13 bits, 2 bytes).
... 254	Reserved

Table 4: Locally Unique / Experimental Identifiers
### Reserved for Future Use Identifiers
IdType Value	Type of Id / Description
255	Reserved for future use

Table 5: Reserved for Future Use Identifiers
# Internal Interfaces
## OLSR Position Update Messages
The OLSR position update messages constitute the 'wire format', which is packed and has conversions applied to the data of the NMEA sentences that are received from the non-OLSR network (see Figure 2 on page 5).
The wire format is described in the 'wireFormat.h' include file. Only the conversions on the data are described in this document.
Below an overview is given of the wire format and in the sections afterward the non-trivial fields will be described.
Field	Bits	Description
version	8	The version of the message format, currently fixed to zero.
updateTime	8	The validity time of the message, with the same semantics as the 'Update Time' field in Table 2 on page 10.
smask	8	A mask signaling the contents of the message.
flags	8	A mask signaling extra contents of the message.
time	17	The timestamp of the position update data: the number of seconds after midnight.
lat	28	Latitude of the position update.
long	27	Longitude of the position update.
alt	16	Altitude of the position update (in meters)
speed	12	Speed of the position update (in kph).
track	9	Track (direction) of the position update (in degrees).
hdop	11	HDOP of the position update.
nodeIdType	8	The type of the nodeId field, see section 2.4.
nodeId	variable	The nodeId for the node that is sending the position update.

Table 6: Position Update Message Format Overview
### updateTime
The update time is mapped non-linearly on the number of available bits according to the following relation (lsn = least significant nibble, msn = most significant nibble).

lsn = validityTime_olsr modulo 16 newline msn = validityTime_olsr over 16 newline validityTime_nmea=((lsn+16) * 2^msn)-16 Formula 1: Update Time Mapping
### smask
The smask field is a mask signaling the contents of the position update message and describes from which types of NMEA sentences the information is taken: each type of NMEA sentence carries different (but not necessarily distinct) information.
Bitfield	Value	Description
GPGGA	1	GGA - Essential fix data which provide 3D location and accuracy data
GPGSA	2	GSA - GPS receiver operating mode, SVs used for navigation, and DOP values
GPGSV	4	GSV - Number of SVs in view, PRN numbers, elevation, azimuth & SNR values
GPRMC	8	RMC - Recommended Minimum Specific GPS/TRANSIT Data
GPVTG	16	VTG - Actual track made good and speed over ground

Table 7: smask bit fields
The smask value is a bit-wise OR of relevant bitfields.
### flags
The flags field is a mask signaling extra contents of the position update message.
Bitfield	Value	Description
GATEWAY	64	The message originates from an external gateway.
ID	128	The nodeIdType and nodeId fields are present.

Table 8: flags bit fields
The flags value is a bit-wise OR of relevant bitfields.
### time
Upon conversion from NMEA sentence to position update message the time field takes the incoming timestamp and converts it to the number of seconds after midnight.
Upon conversion from position update message to NMEA sentence the incoming time (number of seconds after midnight) is added to midnight of the current day. Corner case dealing with day crossings and clock skew are accounted for:
- When the current time is [00:00:00, 12:00:00] and the received time is more than 12 hours after the current time then the received message was sent the day before and the timestamp is adjusted accordingly. This is a day crossing scenario.
- When the current time is <12:00:00, 23:59:59] and the received time is more than 12 hours before the current time then the received time was sent the day after and the timestamp is adjusted accordingly. This is a clock skew scenario.
### lat / long
The latitude and longitude from a NMEA sentence are mapped onto a certain number of bits (see Table 6) in a position update message according to the formulas shown below.

lat_nmea in [-90,~90] newline lat_olsr in [0,~2^bits - 1] newline lat_olsr = (lat_nmea over 180 + 1 over 2)~times~2^bits newline lat_nmea = ({lat_olsr + 1 over 2} over {2^bits} - 1 over 2)~*~180 Formula 2: Latitude Mapping
long_nmea in [-180,~180] newline long_olsr in [0,~2^bits - 1] newline long_olsr=(long_nmea over 360 + 1 over 2) times 2^bits newline long_nmea=({long_olsr + 1 over 2} over {2^bits} - 1 over 2) *360 Formula 3: Longitude Mapping
Note that before conversion from NMEA sentence to position update message the latitude and longitude are converted first to degrees and then to the required ranges as shown in the formulas.
### alt
The altitude is simply offset by a fixed amount of 400 meters such that zero in the position update message means -400 meters in the NMEA sentence.
### hdop
The HDOP is linearly mapped on the number of available bits according to the following relation.

resolution = 0.1 newline hdop_olsr = hdop_nmea over resolution newline hdop_nmea = hdop_olsr times resolution Formula 4: HDOP Mapping
### nodeIdType and nodeId
See section 2.4; both fields are not present when a nodeIdType of 4 or 6 is configured.